## Slide 1: Ece2071 Project
Presented by Team B14

## Slide 2: Introduction and Task review

## Slide 3: What is the project
Creating an audio capturing system that records and outputs recorded sounds through the storage and manipulation of data in STMS
Task 1: Create a MVP that records in a sampling STM, sends to a processing STM, and finally to a python script as a .wav file
Task 2: Create an interface in python (CLI), add features based on proximity (USS), bonus features for analysis
Task 3: Improve quality to 10 bits and downsize
Task 4: Improve quality to 12 bits at a sampling of 44.1 ksps

## Slide 4
Task 1:Minimum Viable Product (MVP)

## Slide 5
Sampling STM:
Using the ADC, music samples were recorded through a bias circuit and transmitted over USART1 using a TX-to-RX pin connection.
Processing STM:
The Processing STM received the samples over USART1 and applied a moving average filter by adding the current sample to the previous sample and dividing the result by 2. The filtered data was then transmitted to the Python script via USART2 (USB connection).
Python Script:
Python functions were used to convert the incoming byte data into WAV files, allowing the recorded audio to be played back and analysed.

## Slide 6
Image 1: Block diagram of process